## Slide 1
Intro to Reliability
30 August 2020

## Slide 2: Reliability Definition
Is the probability an item (e.g., system, subsystem, or component) will perform its intended function with no failure for a stated period of time (or number of demands or load) under stated environmental conditions. Other words, reliability is the probability an item will be in an uptime state (i.e., fully operational or ready to perform) for a stated mission.

## Slide 3: Reliability Break Down
RELIABILITY
The Probability
(used to make 1 of the 2 axes of a risk matrix)
Qualitative Reliability
Perform a bottom-up analysis to show the effect(s) of the item’s failure
Failure Mode and Effects Analysis (FMEA)
Perform a top-down analysis to show how item(s) contribute to a specific failure event
Fault Tree Analysis (FTA)
Quantitative Reliability
Make and use a custom failure-rate function using item’s test and operational data
Demonstrated Reliability
Use handbooks to obtain constant failure rates (adjusted for various conditions)
Predicted Reliability
An item will perform its intended function
Multiple components mapped to form a system
Reliability Block Diagram Analysis (RBDA)
For a stated mission time (duration as time or cycles) or stress (load)
Under stated conditions (environment).

## Slide 4: Reliability as a Function within SWPC
To learn
To improve
To resolve

## Slide 5: Reliability as a Function within SWPC

## Slide 6: Why

## Slide 7: Safety
We often hear,
“Reliable Plant is a Safe Plant”
But how is that ?
How can this effect the personals and the plant ?
Can we do something about it ?

## Slide 8
Safety
SLIPS/TRIPS
PROCESS SAFETY
MANY
FEW
INJURY BUT NOT DEADLY
DEADLY
3X DURINNG NON PLANNED
PROBABILITY INCREASE WHEN RELIABILITY DECREASSE
Safety

## Slide 9
EXAMPLES…
Safety

## Slide 10: safety

## Slide 11: Personal Safety
Personal Safety.
There is a negative correlation between reliability and injures rate.

## Slide 12: Personal Safety
Personal Safety.
There is a negative correlation between reliability and injures rate.

## Slide 13: Process Safety
Process Safety.
The figure below show how the Probability of Failure on Demand (PFD) increase with time.
Once the proof test conducted; the reliability is restored.

## Slide 14: Process Safety
Process Safety.
The figure below show how the Probability of Failure on Demand (PFD) increase with time.
Once the proof test conducted; the reliability is restored.
Similar to the proof testing tasks:-
Condition monitoring
Inspection
Calibration
PMs jobs.
Proof testing
Reliability Decrease
when PFD Increase

## Slide 15: Case Study: Deep Water Horizon
On April 20, 2010
11 killed and 17 Injured
Due to the failure of the Safety Instrumented System (SIS).
This failure was linked to inability to perform functional test.
The design of the BOP control system did not allow independent functional testing of its redundant AMF/deadman subsystems either while the BOP was on the rig or while it was in subsea service. There were four separate emergency subsystems which could activate the AMF/deadman; there were two control pods, each with its own 27 volt battery pack, and each of these two pods had two independent subsea electronics modules (SEMs), each with its own programmable logic controller (PLC), AMF/deadman card and 9 volt battery pack. However, the four subsystems could not be independently tested using the BOP control system. Without independent functional testing for each of these four subsystems, latent failures which disable as many as three of these redundant systems could still result in a successful overall AMF/deadman test result. A successful test even with no working redundant backups would fail to reveal that the reliability of the AMF/deadman emergency safety was severely compromised. *

## Slide 16: Deep Water Horizon
Video

## Slide 17: Availability
AVILABILITY is % of time where the equipment is available for use.
To calculate it we need 2 things:-
Operating Cycle (Time between TAs)
Up Time (time the equipment were running)

## Slide 18: Availability
=
$

## Slide 19: Availability Example
Operating cycle = 8 hours daily for 1 week = 8 x 7 = 56 hours.
1 pump
12 Ton per/H, 1Ton = 100 SAR
1 failure per 16 hours.
To fix it we need 2 hours.

## Slide 20: Availability Example
Time
56
1
0
Failure
Failure
16 Hrs.
2 Hrs.
Maintenance
Maintenance

## Slide 21: Availability Example
Time
56
1
0
Failure
Failure
16 Hrs.
2 Hrs.
Maintenance
Maintenance

## Slide 22: Availability Components
Less Failure,
Less Maintenance Time
Result High Availability
= +
AVILABILITY RELIABILITY MAINTEANBILITY

## Slide 23: Availability Components
SAFETY
RELIABILITY
MAINTENABILITY
AVIALABILITY
Design
Condition monitoring
Inspection
Calibration
PMs jobs.
Proof testing
Precision.
What we Can Improve
Result
Design
Procedures
Planning
TPM
Automation
Move CM to PM/Pdm

## Slide 24: Root Cause Analysis

## Slide 25: Investigation cycle
Experience
Observe
Analyze
Insight
Conclusion
Decision
Action
Generalization

## Slide 26: Problem Statement
WHEN
WHERE
PROBLEM STATEMENT
WHAT
EFFECT
On 5th/March/2019 at 22:00 hrs. in plant x RO shelter 6 Racks tripped for 12 hours and resulted in losing 200,000 m3 of water.

## Slide 27: Logic Tree
1. Describe the Event
2. Describe the Modes
3. Hypothesize
4. Verify the Hypotheses
.
5. Determine Physical Roots
and Verify
.
.
6. Determine Human Roots
and Verify
7. Determine Latent Roots
.
.
How Could?
How Could?
How Could?
Why ?
Fact Line
Fact Line
Fact Line
Fact Line
Fact Line

## Slide 28: System life cycle

## Slide 29: System Reliability
A CHAIN IS ONLY AS STRONG AS ITS WEAKEST LINK

## Slide 30
LINK |  |  |  |  | 
TENSILE STRENGHT N/m2 | 60 | 70 | 55 | 45 | 30
Tensile
Stress
50 N/m2
Which link will break ?
Example

## Slide 31: System Reliability

## Slide 32: Life Cycle

## Slide 33: Bathtub Curve
PROBABILITY OF FAILURE
TIME
Design
Derating
Installation
No experience
Testing
Standards
Procedure
Training
Warranty Management

## Slide 34: Bathtub Curve
PROBABILITY OF FAILURE
TIME
Out of operating window
Wrong maintenance
Strictly following the procedures.
CMs

## Slide 35: Bathtub Curve
TIME
Aging like everything
PMs
CMs
Generally taking care of the old assets.

## Slide 36: Mobile Exercise

## Slide 37: Thank you